## Slide 1: final project
Blake Arledge

## Slide 2: Project Motivation
I began taking up a interest in foreign exchange trading (FOREX) in high school
This form of trading soon led me towards learning more about the world of “trading robots”, which is formally known as “algorithmic trading”
Algorithmic Trading: automated trading by computers which are programmed to take certain action in response to varying market data
  Subset of algo trading is HFT
HFT: an algorithmic trading strategy that emphasizes high transaction volume, extremely short-duration positions, and rapid rule-based automated buying and selling. Accounted for 70% of all trades made in the 2010 FY

## Slide 3: What my project aims to do
My project aims to simulate one portion of the algorithmic/HFT trading network environment
Idea was to have a program take in a stream of Raw Ethernet packets and process the packets with the goal of low latency response.
The approach that I had taken was that the majority of the optimization of response time would be on the sender end. For this reason, I started by focusing on how to send the information in a way that made it easier to respond quickly
  Solution: Ethernet header/metadata formation

## Slide 4: HoW it was done
Initially the plan was to use a program that sent ethernet packets to my machine, however I quickly realized that this could not be done with one machine
  This led to the use of virtual machines (plural)
  I set the experiment up with one vm that would send packets through the socket set up with the virtual ethernet port, the other would sit in idle mode until it started receiving packets and would then return some data to the sender
  This led me to having to learn more about internal networks & virtual machine network systems as a whole

## Slide 5: Technologies utilized
Raw Ethernet
VirtualBox
  Virtual machines
  Internal network setup & use
Linux C-based hardware libraries
tcpdump
Vagrant

## Slide 6: Project pivot
At first this project was intended to be focused on the processing of packets
  However, it quickly became focused on the setup of the virtual machine environment
  The vm’s have virtualized hardware renditions, which tend to be very “finicky” in certain situations
Because the system is so abstracted through the virtualization process, it is often quite easy to get confused as to what the steps are to accomplishing what you originally thought was a simple task

## Slide 7: Take away
My main takeaway from this project, was just how complex these network systems truly are
Furthermore, it made me realize how difficult of a task testing new algorithms on this system could actually be
Sometimes emulation leads to having to address more problems with the virtual system than actually addressing the problems that you had originally planned on exploring